## Slide 1
Ready to answer some questions, maggots ?

## Slide 2
a) units of viscosity
b) glass transition temperature
c) works out stress
d)measures Tg
e) diffraction lines & crystal structure
f) breaks up former bonds
g)re-connects islands
h) 40,000X-100,000X magnifications
Match these terms and acronyms with the short descriptors listed below:
DSC_____ modifier_____ SEM____ flux ____
XRD ____ Tg _____
anneal temperature___ poise____
d
g
h
f
e
b
c
a

## Slide 3
Glass Technology and Measurement drill and practice
In classical glass theory, a glass is composed of three components. In order from most to least in %, what are they ?
Former
  flux
modifier
Given the above component types, which type is SiO2 (sand) ?
Former
What role does flux play in glass making ?
Breaks up extended former network so the glass will
form isolated ‘islands’ and melt at lower temperatures
Give an example of a flux material.
Na2O (soda) K2O (alkali oxides)

## Slide 4
Glass Technology and Measurement drill and practice
What role does the modifier play in glass making ?
They re-join some of the isolated islands created by the flux and stiffen/strengthen the glass
Give an example of a material that serves as a flux
CaO (lime), MgO, BaO (alkaline earth oxides)
Does it make sense that the most common (and oldest) commercial glass is called `soda lime’ glass ? Explain.
Yes. Flux =15% w/w Na2O (soda)
Modifier= 10% w/w CaO (lime)
Former= 75% w/w sand

## Slide 5
Glass Technology and Measurement drill and practice (cont.)
Glass is non-thermodynamic, non-crystallographic and non-____________________
stoichiometric
In the ternary phase diagram below, the increasing glass-forming regions defined by the dark curves is created by…
Increasing the rate of quenching the glass melt

## Slide 6
Glass Technology and Measurement drill and practice (cont.)
This 50,000X micrograph of Pyrex reveals what key structural feature of the glass ?
Pyrex is biphasic (hard silica islands filled in with softer soda-silica-borate-CaO regions)
Name and acronym for the instrument shown
Scanning Electron Microscope (SEM)
SEM’s Typical magnification range ?
1000-40,000X

## Slide 7
Glass Technology and Measurement drill and practice (cont.)
Name the SEM technique leading to each of these images
Back-scattered electrons (BSE)
Secondary electron emission (SE)
X-ray energy dispersion (XRED)

## Slide 8
Glass Technology and Measurement drill and practice (cont.)
Where is the SEM piece in the instrument below ?
What’s this piece do ?
XRED unit (analyzes elemental composition at SEM focus pt)
What’s this for ?
Vacuum coater to spray conductive Au or C onto non-conducting SEM samples

## Slide 9
Glass Technology and Measurement drill and practice (cont.)
Dehydration (exo)
melting
What technique made the curve below ?
Q
Differential Scanning Calorimeter
Where does the DSC sample go in the DSC instrument shown to the right ?
Tg stands for…
Glass transition T
Tgc stands for…
Glass crystal transition T
Tm stands for…
Melting point

## Slide 10
Glass Technology and Measurement drill and practice (cont.)
Find Tg, Tgc and Tm on the DSC curve below
Tg
Tgc
Tm
What’s this instrument called ?
X-ray-diffractometer (XRD)
Point to where source, camera and sample are likely to be here
source
camera
Sample here

## Slide 11
Glass Technology and Measurement drill and practice (cont.)
Phase of sample ?
crystalline
Which XRD scan is created by a pure glass ?

## Slide 12
If life is a bowl of cherries,
why am I always in the pits ???