## Slide 1
Gas Chromatography (GC)

## Slide 2
Honestly, officer, I ain’t drunknk
GC `apps’
in the real
world
Alcohol
Breathalyzer
Replaces old school
`balloon test’ for alcohol

## Slide 3
…what is this portable GC detector looking for ???
Portable Cannabis (THC) GC detector

## Slide 4
The ORIGINS OF GAS “CHROMATOGRAPHY”
What chemicals are in…..???
??????

## Slide 5
First, easiest approach:
Paper chromatography...separates bands
(but hard to collect sample components)
Chroma= color

## Slide 6
Packed column
(originally packed with Confectioners sugar=
`stationary phase’)
Plant extract in ether/hexane mix
Russian Botanist Mikhail Tswett (1872-1919)
The ORIGINS OF GAS “CHROMATOGRAPHY”: packed column separations
Transducer= eyeball
“I did this first ! Da! Da !”
Here, the ether/hexane mix is the `mobile phase’

## Slide 7
Packed glass columns can come in all kinds of sizes

## Slide 8
Schematic of Typical Modern Gas“Chromatograph” (GC)
Proportionating valve
Flow controller
Sample injection
GC column
Primary Helium
Column oven
(thermal ramp)
Detector
Data system and instrument control
Step down P from 160050 psi
Split flow : discard most (typical split 20:1 100:1)
T
t(min)
Level flow to fixed rate
Measure output at selected transducer vs. background He

## Slide 9
HP 5890A GC with FID detector
We use single port injector, not auto samplers
In HP 6890N GC
(ASC): computer controls all flow and pressure via “Chemstation”

## Slide 10
Main Components of a ’GC’
Plumbing to handle gases
Column (heart of GC => separation)
Oven (makes thermal ramp to produce SSS =Sharp, Symmetric, Separated peaks)
Detectors (to see components once they are separated)

## Slide 11
Very strong spring
weaker spring
Compensating springs
Primary tank
Valve controls here
secondary tank Valve
secondary
primary
Plumbing
Controlling the carrier flow part 1:
Tank Valves

## Slide 12
10 mL
mark
He flow from test port of GC
Controlling the carrier flow part 2
old school: flow meters
A soap bubble flow meter (bubble-ometer)
Compute flow:
10 mL/8 seconds= 1.25 mL/s
=75 mL/min
Soap solution in here

## Slide 13
Controlling the flow part 2: split-splitless inlet system- Modern way to control sample volume
and carrier flow
Most of He flow diverted to reduce flow into capillary

## Slide 14
Plumbing part 3: Hooking things up
National Pipe Thread (NPT) fittings… tank fitments

## Slide 15
Swagelok-NPT adapter
ferrule
Back cap
Plumbing part 3 –hookups :Swagelok fittings
FYI..ASC GC, MS and HPLC plumbing is all 3/16” OD…and use 7/16” nut wrench
Nut

## Slide 16
Ferrules for capillary columns are made of carbon (lower crush pressure)
Plumbing part 3-hookups : Ferrules

## Slide 17
Columns-heart of a GC: There are 3 species
Packed, Glass
Packed, metal
Open, capillary (glass)
Packed: typically 0.3-2 m long,
3/16-1/4” OD, stationary phase on support (usually diatomaceous earth
Open, 30-100 m long
0.25 mm ID, stationary phase on inside (0.2-0.3 um)

## Slide 18
Jaap de Zeeuw, a Dutch chromatographer with Restak (commercial column manufacturer), holds the Guinness Record for longest capillary column in the world (1.3 km)

## Slide 19
Columns (continued)
Important acronym: MAOT = Maximum Operating Temperature (Typically < 400 oC)…
Beyond that, the stationary active phase delaminates or cooks off . (You see this in MS…as siloxanes)
`FSWC’ type most common
(Fused Silica Wall Coated
Most common

## Slide 20
0.25 mm
0.00025 mm
(outside)
(inside)
0.35-0.37 mm
Column dimensions
and MAOT written on
column tag or box
(Most stored on computer so that flow and pressures can be computed)

## Slide 21
The liquid phase is the stationary phase. Physically `painted’ onto the silica (wall coated):Typical thickness are 0.25 m
Columns (continued)
`support’ = inner silica wall

## Slide 22
Columns (continued)
Silica wall is often treated with silanizing agent to prevent sample sticking to it (a big problem early on with FSWC columns)
The silanized support is post-coated with the stationary phase and an initial thermal conditioning is applied to new columns to allow stationary phase and silanizing agent to bond/fuse

## Slide 23
The GC Oven
The GC oven is used to create thermal ramps

## Slide 24
What’s a Thermal Ramp and why do we need it ?
Sample mix injected at fixed temperature T=70 oC (isothermal)
I(pA)
time
Injected here
140 oC
40 oC
Sample mix injected with thermal ramp applied (40 oC 140 oC over 10 min =>
ramp=10 oC/min)
10’
I(pA)
time

## Slide 25
Thermal ramps help us achieve SSS
GC peaks are:
Sharp
Symmetric
Separated

## Slide 26
Held to bake/purge column
Held at low T initially to stabilize column and lets lighter species get a head start
A typical `real life’ thermal ramp and resultant chromatogram

## Slide 27
What’s behind the white door…
A large thermally stable volume
GC Oven…what it really looks like
HP 6890 GC with single inject port
GC Oven and Fan

## Slide 28
If no oven needed, GC can be very portable

## Slide 29
With oven…not so portable

## Slide 30
Thermocouple GC Detectors
(passive temperature change)
System is nulled when no sample through column side. The change in Voltage across `Signal’ means Column vs. Ref out of balance
The trusty Wheatstone bridge makes another appearance

## Slide 31
Brief aside on the Wheatstone Bridge
The details on how it works:
1) Variable Ru created by sample changing Ru . Syststem is initially `nulled’ by using Rv
A
B
Rv (or time , t)
I(mA)
2) Current (or voltage) is plotted vs.time as resistance at Ru changes . This produces a signal dependent on Ru. As Ru changes in => spectrum or chromatogram
(Ru)
Rv
0 ?
0

## Slide 32
Wheatstone bridge details(continued)
Using Kirchoff’s laws for voltage and current sums at nodes…
Can solve for numerical value of Ru using the recipe
(where Rv is at null point):
Ru = Rv*R2
R1
(Ru)
Rv
I=0

## Slide 33
Wheatstone bridge details (cont.)
What a basic Wheatstone bridge set-up really looks like

## Slide 34
Dynamic Base line (null) correction with op amp
Mechanical strain gauge
micro pressure sensor : heart monitor
Wheatstone bridge details (cont.)
The `bridge’ is everywhere in modern equipment
All digital voltmeters & voltage displays (DVM)

## Slide 35
Wheatstone bridge is courtesy of Sir Charles Wheatstone…1833 !!
Even if something is ancient, it doesn’t mean it isn’t awesome. The Wheatstone bridge is still one of the best ways to null a circuit.
185 years old and still awesome ,you
snotnosed, young whippersnappers !
Wheatstone bridge details (cont.)

## Slide 36
FID=Flame Ionization Detector
(what we use in ASC lab)
Particularly good for…
Alkanes
Alcohols
Ketones, aldehydes
Ethers
Low weight aromatics
Less good for…
Large aromatics
Herbicides
Pesticides
Organic acids

## Slide 37
Basic Design of an FID
(DC current in pA)

## Slide 38
collector
Sample with carrier gas in here
Air + H2 in here
Igniter (?)
current out here
A real FID

## Slide 39
MSD Mass Selective Detector
(also part of ASC detectors)
Detector of choice in drug analysis
(MSD IDs drugs)
GC
MSD

## Slide 40
PID=Photoionization Detector
(ASC got-no use for now)
Blind to alcohols, alkanes, ketones (ALIPHATICS)
Good with aromatics
(including many herbicides and pesticides

## Slide 41
I, pA
time
100 ppm toluene in ethanol
ethanol
Sketch of typical PID chromatogram

## Slide 42
PID quartz envelope in the flesh…

## Slide 43
ECD=Electron Capture Detector (ASC used to have..no $)
63 Ni*  63Cu + e- (radioactive decay of a beta particle=electron)
e- + X  X- causes change in current from background
Is 10-1000X more sensitive than FID
Particularly good with agricultural chemicals * (but generally useful)
*Herbicides
Pesticides
Drawback: needs US Atomic Energy Commission Government License => $$$$

## Slide 44
Common GC detectors summarized
FID (Flame Ionization Detector) alkanes, alkenes, alcohols, ketones, aldehydes
TCD (Thermocouple Detector) any compound with vapor pressure
PID (Photoionization Detector) aromatics
MSD(Mass Selective Detector) any compound with
  vapor pressure
ECD(Electron Capture Detector) pesticides, herbicides
Detector
What it detects best

## Slide 45
What do cats and chromatography scientists have in common ?
Separation anxiety, of course !