## Slide 1
I know, I know all this MS stuff, teacher…pick me, pick me !!!

## Slide 2
Mass Spectroscopy (MS) Q & A
There are three basic MS designs. Name them in order from most expensive to least expensive.
Magnetic sector
Quadrupole
Time-of-flight
Which design is resident in the ASC instrumentation lab ?
Quadrupole
For all three of the basic MS designs, what is the most common fragmentation method/source?
Electron Impact (EI)
Name one drawback of EI
Collisions can erase Parent mass
Name a fix to this problem and how it works
Chemical ionization (with methane)…a much softer collision reduces energy and saves parent

## Slide 3
Mass Spectroscopy (MS) Q & A (cont.)
Which is the EI source ?
Use this to explain how the EI source works

## Slide 4
Mass Spectroscopy (MS) Q & A (cont.)
Name these various bits of GC-MS plumbing
Swagelok fitting
NPT fitting
Con-flat fittings
Which is necessary for high vacuum part of MS ?

## Slide 5
Mass Spectroscopy (MS) Q & A (cont.)
Magnetic sector
quadrupole
Time-of-flight
What kind of MS am I ?

## Slide 6
Mass Spectroscopy (MS) Q & A (cont.)
Match the schematic to the MS type
Quadrupole MS
TOF (Time-of-Flight) MS
Magnetic sector MS
Briefly explain how each schematic outlines the manner in which mass selection occurs.

## Slide 7
Mass Spectroscopy (MS) Q & A (cont.)
What is the first thing you monitor when starting up any MS ?
Vacuum chamber pressure
Why is achieving a low vacuum chamber pressure critical ?
EI needs clear path to collide with samples. A poor vacuum leads to low signal and can burn out source
Two different combinations of pumps are used ASC Quad MS . What are they ?
Mechanical (direct drive) + oil diffusion (ELANOR)
Mechanical (direct drive) + turbomolecular (Bob and Babette)
What vacuum level is `acceptable’ for our Quad MS?
~(15)*10-5 torr

## Slide 8
Mass Spectroscopy (MS) Q & A (cont.)
Name the pump…
Mechanical pump
diffusion pump
Turbomolecular pump
Cryo pump
Titanium sublimation (getter) pump

## Slide 9
Mass Spectroscopy (MS) Q & A (cont.)
Which pump is associated with these schematics ?
Oil diffusion
mechanical
Turbomolecular

## Slide 10
Mass Spectroscopy (MS) Q & A (cont.)
What are our names an what do we measure ?
TC (thermocouple) pressure gauge
Phillips-Granville Vacuum tube pressure gauge
Which measures the pressure at high pressure ?
Which kicks in at very low pressures ?

## Slide 11
Mass Spectroscopy (MS) Q & A (cont.)
What does this doohickey do in the MS ?
Dynode multiplier detector
Use the text’s schematic of the above and explain how it works.
Detects m+
What’s its official name ?

## Slide 12
Mass Spectroscopy (MS) Q & A (cont.)
Briefly explain ion generation with this diagram

## Slide 13
Mass Spectroscopy (MS) Q & A (cont.)
Briefly explain ion acceleration with this diagram

## Slide 14
Mass Spectroscopy (MS) Q & A (cont.)
From accelerator/ion focusing
M1+ , M2+ ,M3+ …
Briefly explain how various M+ are `selected’ with this diagram

## Slide 15
,DOC