## Slide 1
The ORIGINS OF GAS “CHROMATOGRAPHY”
What chemicals are in…..???
??????

## Slide 2
First, easiest approach:
Paper chromatography...separates bands
(but hard to collect sample components)

## Slide 3
Packed column
(originally packed with Confectioners sugar=
`stationary phase’)
Plant extract in ether/hexane mix
Russian Botanist Mikhail Tswett (1872-1919)
The ORIGINS OF GAS “CHROMATOGRAPHY” : column separations
Transducer= detector= eyeball
“I did this first ! Da! Da !”
Here, the ether/hexane mix is the `mobile phase’

## Slide 4
Schematic of Typical Modern Gas“Chromatograph” (GC)
Proportionating valve
Flow controller
Sample injection
GC column
Helium
Column oven
(thermal ramp)
Detector
Data system and instrument control

## Slide 5
HP 5890A GC with FID detector
We use single port injector, not auto samplers
In HP 6890N GC
(ASC): computer controls all flow and pressure via “Chemstation”

## Slide 6
Main Components of a ’GC’
Plumbing to handle gases
Column (heart of GC => separation)
Oven (thermal ramp to aid
separation)
Detectors (to see components once they are separated)

## Slide 7
Very strong spring
weaker spring
Compensating springs
Primary tank
Valve
secondary tank Valve
secondary
primary
Plumbing:Tank Valves

## Slide 8
Plumbing: National Pipe Thread (NPT) fittings

## Slide 9
Swagelok-NPT adapter
ferrule
Back cap
Plumbing:Swagelok fittings
FYI..ASC GC, MS and HPLC plumbing is all 3/16” OD…and use 7/16” nut wrench
Nut

## Slide 10
Ferrules for capillary columns are made of carbon (lower crush pressure)
Plumbing: Ferrules

## Slide 11
Plumbing: split-splitless inlet system:
Modern way to control sample volume

## Slide 12
Columns: There are 3 species
Packed, Glass
Packed, metal
Open, capillary (glass)
Packed: typically 0.3-2 m long,
3/16-1/4” OD, stationary phase on support (usually diatomaceous earth
Open, 30-100 m long
0.25 mm ID, stationary phase on inside (0.2-0.3 um)

## Slide 13
Columns (continued)
MAOT = Maximum Operating Temperature (Typically < 400 oC)…
Beyond that and stationary active phase delaminates or cooks off
`FSWC’ type most common
(Fused Silica Wall Coated

## Slide 14
The liquid phase is the stationary phase. Physically `painted’ onto the silica (wall coated):Typical thickness are 0.25 m
Columns (continued)
`support’ = inner silica wall

## Slide 15
Columns (continued)
Silica wall is often treated with silanizing agent to prevent sample sticking to it (a big problem early on with FSWC columns)
The silanized support is post-coated with the stationary phase and an initial thermal conditioning is applied to new columns to allow stationary phase and silanizing agent to bond/fuse

## Slide 16
What’s behind the white door…
GC Oven…how we make a thermal ramp
HP 6890 GC with single inject port
GC Oven and Fan

## Slide 17
2 min Initial Hold time
What’s a Thermal Ramp and why do we need it ?

## Slide 18
Thermocouple GC Detectors
(passive temperature change)
System is nulled when no sample through column side. The change in Voltage across `Signal’ means Column vs. Ref out of balance

## Slide 19
FID=Flame Ionization Detector
Particularly good for…
Alkanes
Alcohols
Ketones, aldehydes
Ethers
Low weight aromatics
Less good for…
Large aromatics
Herbicides
Pesticides
Organic acids

## Slide 20
MSD Mass Selective Detector
Detector of choice in drug analysis
(MSD IDs drugs)

## Slide 21
PID=Photoionization Detector
Blind to alcohols, alkanes, ketones (ALIPHATICS)
Good with aromatics
(including many herbicides and pesticides

## Slide 22
ECD=Electron Capture Detector
63 Ni*  63Cu + e- (radioactive decay of a beta particle=electron)
e- + X  X- causes change in current from background
Is 10-1000X more sensitive than FID
Particularly good with agricultural chemicals * (but generally useful)
*Herbicides
Pesticides
Drawback: needs US Atomic Energy Commission Government License